## Slide 1: Reading Report 6
A Physics-Guided Deep Learning Predictive Model for Robust Production Forecasting and Diagnostics in Unconventional Wells

## Slide 2: Introduction
Goal:
  Predict well performance to improve reserves estimation and optimize production
Solution:
  A physics-guided deep learning model that integrates well properties to forecast production
Key Features:
  Multi-task learning (forecasts production, estimates reserves, aids diagnostics) and Extended Capability to handle properties outside the training data range
Application:
  Tested on Bakken Shale Play data for robust, accurate forecasts

## Slide 3: Challenge of Hydrocarbon Production
Problem:
  Conventional reservoir models introduce significant errors when applied to unconventional reservoirs
Challenges:
  Complex fracture networks and geomechanical interactions make predictions difficult
  Existing simulations are based on assumptions for conventional reservoirs, leading to inaccurate forecasts

## Slide 4: Deep Learning to the Rescue
Solution
  A deep convolutional neural network (CNN) helps to improve predictions by:
    Simulation errors
    Oil production
    Well success rates
Impact
  Multi-Task Learning: Tackles multiple predictions at once—saving time and improving accuracy
  Augments Traditional Models: Blends physics with data insights for way better forecasts

## Slide 5: Production Prediction Model
Model Components
  Inputs (I₁):
    Well properties (𝒙 ∈ 𝑹,ₙ), processed through fully-connected layers
  Prediction Outputs:
    O₁: 1D Convolution for simulation error prediction (oil, water, gas)
    O₂: Scalar output for cumulative oil production (𝑦 ∈ 𝑅₁)
    O₃: Class label (low/mid/high performing wells)
Training
  Implemented using Keras in Python
  Loss Functions:
    Mean-squared error for regression, cross-entropy for classification
  Multi-task loss optimization to improve all predictions simultaneously

## Slide 6: Results
Data Source
  Bakken field data, including perforation length, proppant volume, treatment pressure, stages, and gamma-ray readings
Model Performance
  Low prediction RMSE for the test set and scatter plots confirm strong prediction performance despite data noise
Future Enhancements
  ~95% accuracy in classifying wells as low, mid, or high performers and misclassifications due to noisy data and complex relationships
Prediction Accuracy
  Model corrects simulation errors and effectively predicts cumulative oil production

## Slide 7: Classification Results
Chart: Training Data
| Actually C#1, Predicted C#1 | Actually C#1, Predicted C#2 | Actually C#2, Predicted C#1 | Actually C#2, Predicted C#2 | Actually C#3, Predicted C#3
Value | 0.15 | 0.05 | 0.03 | 0.37 | 0.4
Chart: Testing Data
| Actually C#1, Predicted C#1 | Actually C#1, Predicted C#2 | Actually C#2, Predicted C#1 | Actually C#2, Predicted C#2 | Actually C#3, Predicted C#3
Value | 0.25 | 0.2 | 0.05 | 0.25 | 0.25

## Slide 8: Conclusion
Research Need
  Further exploration is essential for flow simulation models in tight formations
Hybrid Modeling
  Combines data-driven methods with physics-based models to improve prediction accuracy
Multi-task Learning
  Enhances generalization and reduces training data needs by predicting multiple metrics simultaneously
Future Work
  Larger datasets and validation in complex scenarios are needed to refine the modeling approach

## Slide 9: Quiz Question
Question: What are the reasons why traditional reservoir simulation models might not accurately predict outcomes in unconventional oil and gas resources?
Answer:
  Conventional reservoir simulation models may introduce errors in unconventional resources due to several limitations. They often fail to account for complex fracture networks, which are common in unconventional reservoirs. Additionally, these models rely on outdated mathematical techniques that may not be suitable for the unique characteristics of these resources. Furthermore, traditional models are typically not designed for tight formations, such as those found in shale or tight gas reservoirs. Lastly, they often fail to effectively model geomechanical interactions, which are crucial for accurately predicting behavior in unconventional settings. These limitations can lead to significant inaccuracies when conventional models are applied to unconventional resources.